## Slide 1
US 17/92
PROJECT DEVELOPMENT AND ENVIRONMENT (PD&E) STUDY
PASS THE TORCH MEETING
PD&E to Design Handoff
From Ivy Mist Lane to Avenue A Financial Management No.: 437200-2
Notes: Introductions
Purpose of the meeting: PD&E to design handoff

## Slide 2
Presentation Agenda
PD&E Study Overview
Regional Overview
PD&E Study Preferred Alternative
Major Environmental Constraints
PD&E Commitments
Preferred Alternative Refinement
Public Input
Design Considerations
Open Discussion
Notes: Overview of the PD&E study including regional overview, preferred alternative key decisions, constraints to carry forward, and commitments for the design team to be aware of
After that, we’ll cover how the preferred alternative was optimized, what we heard from the public, and the primary design considerations still needing attention.
We’ll close with discussion and handoff questions.

## Slide 3
PROJECT AT A GLANCE
2 to 4 lane widening
Reedy Creek Bridge
Runs through Intercession City
US 17/92 PD&E Study Overview
Ivy Mist Lane to Avenue A | Osceola County | 3.8 miles
PURPOSE & NEED
Reduce congestion
Address future travel demand
Improve safety & multimodal connectivity
PROJECT STATUS
PD&E Approved
October 2025
Post-PD&E Optimization
June/July 2026
PROJECT LOCATION MAP
Notes: Study limits
Reedy Creek Bridge
Runs through intercession city
Purpose and need to relieve congestion, address future traffic needs, and improve safety and multimodal connectivity
PD&E was approved in October 2025
Post-PD&E optimization earlier this year

## Slide 4
Regional Overview
Notes: This project is an integral part of several regional projects in the area.
Connecting to the east end of the project limits, US 17/92 was recently widened up to Avenue A.
The Poinciana Parkway Extension segment up to CR 532 is being completed by CFX and is currently in design, and is funded for construction in FY 2027. It will connect to US 17/92 with an interchange just south of this project limits and is planned to tie into this widening project.
Poinciana Parkway Extension Connector to I-4, project by the Turnpike is in design
CR 532 widening, being completed by CFX is currently under construction
There is also the Polk County SunRail Expansion PD&E Study currently underway
And the Central Polk East new roadway connection to the Future Poinciana Parkway that recently had approved PD&E study in May of this year

## Slide 5
Existing Roadway
Notes: PPE connection at the west end.
SR 532 widening intersection with US 17/92 just west of the reedy creek bridge
Reedy creek bridge crossing, many constraints we will discuss further
Cemetery
Intercession City
Connection to recently widened US 17/92 to the east.

## Slide 6
Existing Typical Sections
Reedy Creek Bridge
Ivy Mist Lane to West of Intercession City
East of Intercession City to Avenue A
Through Intercession City
Design speed: 60 mph | Posted speed: 55 mph
Design speed: 60 mph | Posted speed: 55 mph
Design speed: 60 mph | Posted speed: 45 mph
Design speed: 55 mph | Posted speed: 45 mph
Notes: Existing typicals
Ivy Mist Lane to Intercession City
Bridge section across Reedy Creek
Through Intercession City
East of Intercession City setup to add and drop lane to recently widened US 17/92 to the east

## Slide 7
General Typical Section
45 mph design, target, and posted speed
Four-lane divided, urban typical sections
Shared-use path and drainage swales on both sides of roadway
Benefits of this typical section included enhanced capacity/traffic operations, increased safety through access management changes, and enhanced bicycle/pedestrian facilities
Proposed profile raised by 2-4 feet
PD&E Study Preferred Alternative
Notes: -

## Slide 8
Reedy Creek Crossing
45 mph design, target, and posted speed
Separate structures to minimize impacts to important cypress trees in area
Restripe existing bridge to eastbound-only traffic
Removal of abandoned bridges north of existing bridge to construct new bridge for westbound-only traffic
12-foot shared-use path only on new westbound bridge
70-foot separation between bridges
PD&E Study Preferred Alternative

## Slide 9
East of Reedy Creek Typical Section
45 mph design, target, and posted speed
151-foot existing ROW
12-foot shared-use path, 11-foot lanes, curb and gutter on both sides of roadway, 22’ raised median
Benefits of this typical section included enhanced capacity/traffic operations, increased safety through access management changes, and enhanced bicycle/pedestrian facilities
Proposed profile raised by 2-4 feet
PD&E Study Preferred Alternative

## Slide 10
Intercession City Typical Section
30 mph design, target, and posted speed
100-foot existing ROW
10-foot urban side path, 11-foot lanes, curb and gutter on both sides of roadway, 15.5’ raised median
Footprint stays within existing ROW for majority of Intercession City, up to 8-foot of ROW acquisition required in several locations
Speed curves leading into Intercession City to encourage lower speed
Access management changes include restricted crossings and two midblock crossings
PD&E Study Preferred Alternative

## Slide 11
Intersections
Stage 2 ICE performed for three intersections
Realignment of CR 532 (Osceola Polk Line Road) approach and signal replacement
Realignment of Old Tampa Highway approach and new signal
Roundabout at Avenue A
PD&E Study Preferred Alt.
Avenue A
Old Tampa Highway
CR 532
1
2
3
1
2
3

## Slide 12
Stormwater Ponds
  Three preferred pond sites
  Meet South Florida Water Management District Standards
Joint Use Ponds
  Two CFX-owned Joint Use Ponds
    JU Pond 1 – Pond 400 will be turned over to FDOT once PPE is complete and need to be expanded as part of this project.
    JU Pond 2A – Pond 7 will be turn over to Osceola County once CR 532 is complete. Pond will need to moved and expanded to accommodate our pond and realignment
Floodplain Compensation Area
LDCA received 10/29/25 – under old stormwater rule
Conceptual Drainage
JU Pond 1
JU Pond 2A
Pond 2B
Pond 3.1
Pond 4.1
Floodplain Compensation 2
Notes: Four-basin wet detention concept
Joint-use ponds with CFX in basins 1 and 2
ROW needed for pond sites
Floodplain compensation area required
LDCA before new rule

## Slide 13
Key Environmental Factors
REEDY CREEK CROSSING
Original US 17/92 alignment is north of existing bridge and consists of 3 historic bridges
Railroad linear historic resource and utility corridors north of original US 17/92 alignment
“Fletcher Park” and county resolutions
  April 11, 1994 – opposing any further removal of large cypress trees in Fletcher Park
  December 18, 2023 – reaffirming support of preserving cypress trees
Archaeological resources
  Beehive Hill and Sub Area A (Preservation Site)
  Beehive Hill Redeposited site
Notes: -Major area of constraint – Reedy Creek crossing
Existing bridge was constructed in 2000s south of the old US 17/92 alignment
Three bridges in old alignment are historic
North of the old alignment is a historic railroad and utility corridors
Fletcher Park area – Osceola County resolution and tree inventory/impact report
The archaeological resource Beehive Hill including Sub Area A (preservation site) is located south of US 17/92 on the east end of the bridge
Just east of the Old Tampa Highway intersection is a Beehive Hill redeposited site

## Slide 14
Key Environmental Factors
REEDY CREEK CROSSING
Numerous bridge alternatives analyzed
Recommendation: Remove/replace 3 historic US 17/92 bridges to accommodate new westbound bridge
FDEP letter of support
  February 25, 2025
  Support PD&E study recommended alternative
  Reiterated opposition to any other alternative that would impact the large cypress trees in Fletcher Park
Any alignment changes over Reedy Creek will have significant schedule impacts and could impact the feasibility of the project.
Notes: A bridge alternatives analysis was conducted
Recommendation is to repurpose the existing US 17/92 bridge for the eastbound and the historic bridges and alignments will be removed/replaced with a new westbound bridge.
FDEP provided letter of support on Feb 25, 2025
Any change to the reedy creek alignment will have significant schedule change.

## Slide 15
Key Environmental Factors
FLOODPLAINS
Floodplain compensation area required
FCA identified during PD&E
Coordinate with property owner/ utility to identify access to proposed FCA
KEY DESIGN TAKEAWAY
Coordinate with Property owner/utility for construction and maintenance access
NOISE
No feasible noise barriers identified
KEY DESIGN TAKEAWAY
No barrier commitment to carry into design
CONTAMINATION
7 medium-risk sites identified
Level 2 assessment required in design
KEY DESIGN TAKEAWAY
Flag risk sites early during design and conducted Level 2 assessments as required
Notes: As mentioned, floodplain compensation area required
FCA site identified and evaluated during PD&E
Coordinate with SWFMD for permitted work over Reedy Creek, as the segment between the abandoned bridges corridor and the existing bridge are Sovereign submerged lands
Noise study found no feasible noise barriers
7 medium-risk contamination sites will require Level 2 assessment in design

## Slide 16
Key Environmental Factors
CULTURAL RESOURCES
Removal/replace of 3 historic results in adverse effect addressed through executed MOA executed on Aug 7, 2025.
Stipulations include:
  Conduct architectural history survey of up to 35 bridges (within 5 years) Underway
  Publicly available historic interpretation of existing historic bridges (within 5 years)
  Archaeological monitoring of the Beehive Hill and the Beehive Hill Redeposited sites during construction
PERMITS
Section 404
Environmental Resource Permit (ERP) – individual under jurisdiction of SFWMD
National Pollutant Discharge Elimination System (NPDES) – CGP to be obtained by contractor
Gopher Tortoise Relocation
FDEP Dewatering Permits
USACE has stated that Reedy Creek is jurisdictional under Section 10 of the Rivers and Harbors Act
Notes: The removal and replacement of the 3 bridges is an adverse effect and a Section 4(f) use.
A MOA executed with SHPO on Aug 7, 2025 addresses the effects.
Stipulations include conducting architectural history survey of up to 35 bridges, documenting and creating publicly available historic interpretation of existing historic bridges and archaeological monitoring of the archeological protected sites during construction.
While the design team may not be responsible for these stipulations, we need to ensure these items are carried forward. First two have to be done within 5 years of execution. The third item should be included in the design notes to the contractor.
Permits include..

## Slide 17
PD&E Commitments to Carry Forward
Cultural & Historic Resources
Avoid permanent impacts to historic cypress trees within Fletcher Park.
Comply with Section 106 MOA stipulations executed August 7, 2025.
Protected Species / Agency Coordination
Apply the most recent USFWS Standard Protection Measures for the Eastern Indigo Snake during construction.
If the tricolored bat is listed as Threatened/Endangered and the Preferred Alternative lies within the consultation area, re-initiate USFWS consultation to determine survey methodology and protective measures.
Re-initiate USFWS consultation for Audubon’s crested caracara and re-survey prior to construction.
If the monarch butterfly becomes listed, re-initiate USFWS consultation to determine avoidance/minimization measures.
Complete Florida bonneted bat surveys during design per USFWS protocol.
Construction Requirements
Require contractor to remove garbage daily or use bear-proof containers to avoid attracting Florida black bears.
Report nuisance bear interactions to FWC Wildlife Alert Hotline: 888-404-FWCC (3922).
If blasting is proposed for bridge demolition, submit a blasting plan and obtain USFWS/FWC approvals prior to construction.
Mitigation
Provide mitigation for wood stork SFH impacts through a Service-approved wetland mitigation bank or wood stork conservation bank within the service area.
Notes: Commitments to carry forward include:
Fletcher Park cypress tree protection
Section 106 MOA compliance
Eastern indigo snake protection measures
Tricolored bat trigger/re-initiation
Audubon’s crested caracara consultation and re-survey
Monarch butterfly trigger/re-initiation
Complete Florida bonneted bat surveys during design
Bear interaction reporting and daily trash removal/bear proof containers during design
If proposed, blasting plan for USFWS/FWC approval prior to construction
Wood stork mitigation banking

## Slide 18
Preferred Alternative Refinement
PD&E Typical Section
Optimization Typical Section
Overview: Post-PD&E optimization developed a condensed urban typical section that fits within existing ROW, excluding proposed pond sites. FDOT is open to rolling back some FDM requirements
Proposed Profile: Proposed profile updated to avoid ROW impacts and minimize use of gravity wall
Benefit: Minimizes property impacts, reduces costs, and expedites delivery
Notes: -Post-PD&E optimization
-condensed typical
-fit within existing ROW (excluding pond sites)
-alignment shift to reduce impacts
-lower property impact
-lower cost
-expedites delivery

## Slide 19
Preferred Alternative Refinement
Optimization Typical Section
Typical Section: 11’ travel lanes, a 15.5’ raised median (reduced from 22’), and 6’ and 10’ sidewalks (reduced from 12’ and 12’) – a reduced footprint to minimize impacts
Alignment Shift: Shifted 5’ south between east of Old Tampa Highway to west of Pond 3.1 to reduce north-side ROW impacts and walling needs
Notes: -Post-PD&E optimization
-condensed typical
-fit within existing ROW (excluding pond sites)
-alignment shift to reduce impacts

## Slide 20
Preferred Alternative Refinement
Optimization Reedy Creek Crossing Typical Section
Reedy Creek Crossing: Same typical as in PD&E – Restriping existing bridge for eastbound traffic, constructing new bridge for westbound traffic
Notes: -retain reedy creek PD&E alignment, with restriping
-Intercession City refinements
-lower property impact
-lower cost
-expedites delivery

## Slide 21
Preferred Alternative Refinement
Optimization Intercession City Typical Section
Intercession City: Intermittent 4-lane typical section with bidirectional left turn lane. Includes 6’ and 10’ sidewalks (reduced from 10’ and 10’). Alignment shifted north to minimize ROW impacts
Notes: -retain reedy creek PD&E alignment, with restriping
-Intercession City refinements
-lower property impact
-lower cost
-expedites delivery

## Slide 22
Public meetings & hearing held within Intercession City and were well attended.
What we heard:
Preferred Alternative Optimization supports concerns for reducing ROW impacts which will also aid in expediting the project.
Intercession City residents would likely approve of the 5-lane section as it provides more access but would still want a signal.
Roadway Access & Safety
Access management concerns in Intercession City
Requests for a signalized intersection in Intercession City
Public Involvement & Sentiment
Pedestrian & Community Impact
Pedestrian safety and accessibility
Avoid impacts to ROW/relocations
Environmental & Quality-of-Life
Existing drainage concerns, particularly within Intercession City
Desire for noise abatement
Project Delivery & Traffic Conditions
Frustration with schedule – desire to expedite
Experiencing heavy traffic conditions
Notes: Meetings and hearings held during PD&E study
Strong participation
Access management concerns within Intercession City
Request for signalized intersection
Ped safety and accessibility concerns
Requests to avoid ROW impacts
Existing drainage concerns
Desire for noise abatement
Frustration with project schedule
Experiencing heavy traffic
Optimization expected to address concerns by reducing ROW impacts and aid in expediting project
Additional coordination with Gatorade Plant manager

## Slide 23
Design Considerations
Adjacent Project Coordination: Continue coordination with CFX and Osceola County regarding the PPE, joint-use pond assumptions, and Osceola Polk Line Road realignment
Reedy Creek Crossing: Maintain approved Reedy Creek bridge concept and location
Alignment/Profile Refinements: Alignment and profile controlled by drainage elevations. Profile estimated to be raised by 1-3 feet
Maintenance of Traffic: Temporary pavement needed in order to construct proposed design and maintain flow of traffic
Notes: Adjacent project coordination
Maintain reedy creek crossing
Wall needs – survey will help
Alignment profile and drainage – survey will help

## Slide 24
Design Considerations
U-Turn Bulbouts: The narrowed 15.5-foot median may not fully accommodate design vehicle turning movements without additional pavement
Intercession City: The PD&E concept showed proposed ROW was needed, while the optimized concept showed it was not. Further survey data will determine if a raised median can be provided.
FCA Coordination: Continue FCA coordination with the utility company and/or property owner to confirm construction and long-term maintenance access
Notes: MOT considerations
U-turn pavement needs
Intercession City – survey will help
FCA coordination

## Slide 25
Open Discussion

## Slide 26
Intersection Control Evaluation
  Intersection treatments considered:
    U.S. 17-92 at Osceola Polk Line Road
    Signal
    Restricted Crossing U-Turn (RCUT)
    U.S. 17-92 at Old Tampa Highway
    Signal
    U.S. 17-92 at Avenue A
    Signal
    Roundabout
    RCUT
    Median U-Turn (MUT)
  Bold = Recommended
1
2
3
1
2
3
ICE Stage 2 Approved - January 4, 2022
FPID No.: 437200-1 U.S. 17-92 PD&E
Notes: The study team conducted an Intersection Control Evaluation in three locations along the corridor. Intersection treatments considered on U.S. 17/92 at Osceola Polk Line Road included a signalized intersection and RCUT. At Old Tampa Highway a signalized intersection was considered and at Avenue A considerations were made for a signalized intersection, roundabout, RCUT, and MUT. The recommended intersection treatments are in bold. with a signal recommended at Osceola Polk Line Road and Old Tampa Highway intersections, and a Roundabout recommended at the Avenue A intersection.

## Slide 27: Click to edit Master title style
FPID No. 437200-2
Existing Intersection Location
532
300’
Notes: As part of the Preferred Alternative, the Osceola Polk Line Road/County Road 532 intersection is proposed to be shifted approximately 300 feet to the west along U.S. 17-92. This recommendation is being made to improve safety conditions at the intersection and provide an improved connection to the bridge over Reedy Creek. The intersection is proposed to remain a signalized intersection and will include an additional dedicated westbound right turn lane and dedicated eastbound left turn lane on to County Road 532.

## Slide 28: Click to edit Master title style
FPID No. 437200-2
Existing Intersection Location
375’
Notes: A new signalized intersection is proposed at U.S. 17-92 and Old Tampa Highway. This new intersection is proposed to be shifted to the east to improve safety and will include a dedicated eastbound left turn lane and westbound right turn lane onto Old Tampa Highway, and dedicated turn lanes from Old Tampa Highway onto U.S. 17-92. A pedestrian crosswalk is included at the intersection to provide a connection to the proposed shared-use path that travels along the north side of the proposed new bridge over Reedy Creek.

## Slide 29: Click to edit Master title style
FPID No. 437200-2
Notes: A roundabout is proposed at the intersection of Avenue A and U.S. 17-92 to enhance safety and operations at the intersection. The center island of the roundabout will be surrounded by a truck apron to accommodate larger trucks. Intersection lighting and pavement markings are recommended to increase visibility and help drivers navigate the roundabout.

## Slide 30: Click to edit Master title style
FPID No. 437200-2
Crossing Treatments
  Two midblock crosswalks proposed
  Pedestrian Hybrid Beacon (PHB)
Recommended Speed Management Practices
  Horizontal deflection
  Speed feedback signs
  Curb and gutter
  Shared-use paths
  Landscaping
Notes: As part of the Preferred Alternative, additional community enhancements were considered within Intercession City to improve pedestrian and vehicle safety. Two midblock crosswalks are proposed; one just east of Tallahassee Boulevard and one just west of Nocatee Street/Shepherd Lane. The midblock crosswalks are proposed to include pedestrian hybrid beacons to alert drivers when crossings will occur. To manage speeds through Intercession City, several speed management practices have been incorporated into the Preferred Alternative, including horizontal deflection, or intentional curves to manage speed, speed feedback signs, curb and gutter resulting in narrower travel lanes, shared-use paths, and landscaping. These speed management practices are intended to slow vehicles by increasing driver alertness. The use of landscaping will be further evaluated in the design phase for this project.

## Slide 31
Preferred Alternative Optimization
Optimization East of Reedy Creek Typical Section
East of Reedy Creek: 11’ travel lanes, a 15.5’ raised median, and 6’ and 10’ sidewalks – a reduced footprint to minimize impacts
Notes: -retain reedy creek PD&E alignment, with restriping
-Intercession City refinements
-lower property impact
-lower cost
-expedites delivery